## Slide 1
EmotiBit Live Dashboard
Real-Time Biosensor Visualization & Recording
Built with Python, PyQt6, pyqtgraph, and BrainFlow

## Slide 2
Data Acquisition & Real-Time Processing
Hardware Abstraction via BrainFlow
• Uses EmotiBit Board ID to interface natively with the hardware.
• Separates streaming channels into three logical presets: Default (IMU), Auxiliary (PPG), and Ancillary (EDA/Temp).
• QTimer event loop polls internal ring buffers at an optimized 40ms interval.
On-The-Fly Digital Filtering
• Filters high-frequency ambient noise and baseline wander from raw PPG channels.
• Employs a 3rd-order Butterworth bandpass filter (0.5 Hz - 5.0 Hz cutoff).
• Uses scipy.signal.filtfilt to perform zero-phase forward/backward digital filtering.

## Slide 3
Interactive Visualization Interface
1. Motion Tab
• Displays Accelerometer (X, Y, Z) in g-forces.
• Displays Gyroscope (X, Y, Z) in deg/sec.
• Hardware-accelerated plot rendering.
2. PPG Tab
• Plots Infrared, Red, and Green pulse waves.
• Applies live bandpass noise-filtering.
• Implements a dynamic Y-axis auto-zoom algorithm to center signals.
3. EDA & Temp Tab
• EDA (Electrodermal Activity) tracks sweat levels.
• Tracks primary & secondary skin temperatures.
• Structured multi-plot grid layout.

## Slide 4
Features & CSV Session Export
System Features
• Live status trackers display Connection, Stream, and Recording states.
• Robust error-handling shields UI from device dropouts or connection crashes.
• Modular architecture separates device communications from front-end layout.
Data Recording & Export
• Allows dynamic session-recording toggle at any point during live streaming.
• Captures comprehensive sensor data (AccX/Y/Z, GyroX/Y/Z, EDA, Temp1/2).
• Exports structured data automatically to CSV, appending the session duration metadata.